## Slide 1: International Accelerator School 2023 Superconducting Science and Technology for Particle Accelerators Linear Optics 1 (1h): Concepts
Todd Satogata (Jefferson Lab and Old Dominion University)
satogata@jlab.org
https://indico.lightsource.ca/event/6/timetable/#20230712
Additional material/courses: http://www.toddsatogata.net/
Happy Birthday to Willis Lamb (1955 Nobel), Buckminster Fuller, and the Australian Aboriginal Flag!
Happy Etch-a-Sketch Day (July 12 1960), New Conversations Day, and Paper Bag Day!

## Slide 2: Outline
Quick refresher from yesterday’s lectures
  Relativity, rigidity, phase space, 1D transport
Thin quadrupoles
Strong focusing
Periodic linear beam transport
Hill’s equation and Twiss/Courant-Snyder revisited
Invariants, emittances (normalized and geometric)
General linear beam transport (parameterization)
Twiss parameter propagation
FODO cell analysis, stability and examples
Periodic triplet optics

## Slide 3: Review: Convenient Relativity Relations
Differential relations are fun to derive, hold for all γ
In “ultra” relativistic limit β≈1
  Usually must be careful below γ≈5 or U≈5 mc2
    For high energy electrons this is only U≈2.5 MeV
  Many accelerator physics phenomena scale with γk or (βγ)k
Total energy
Momentum
are relativistic or C-S/Twiss parameters: context!

## Slide 4: Rigidity: Bending Radius vs Momentum
This is such a useful expression in accelerator physics that it has its own name: rigidity
Ratio of momentum to charge
  How hard (or easy) is a particle to deflect?
  Often expressed in [T-m] (easy to calculate B)
  Be careful when q≠e!!
A possibly useful expression
Beam
Accelerator (magnets, geometry)
Notes: Perpendicular B!
Add q[e] (or Z) to last equation
Be careful; very low-energy people may define rigidity relative to KE rather than p
RHIC: dAu tradeoff

## Slide 5: “Review”: Phase Space (as commonly used)
Yesterday
Phase
space
Paraxial approximation
Always check simulation code/course coordinate systems

## Slide 6: “Review”: (1D) Transport Matrix
is a second-order differential equation
  Linear solutions “transport” (x,x’) initial conditions
  Coordinates are properties of particles/beam
  M is defined by the accelerator lattice
  Chain/multiply lattices together for different elements
x: transverse position
x’: transverse angle, “velocity”

## Slide 7: Thin Quadrupole Transport Matrix
Quadrupoles are often treated as “thin”
  Focal length is much longer than magnet length
Then we can use the thin-lens approximation
  where f=1/(kL) is the quadrupole focal length
Focusing
Quadrupole
Thin quadrupole approximation
Defocusing
Quadrupole

## Slide 8: Matrix Example: Strong Focusing
Consider a doublet of thin quadrupoles separated by drift L
  There is net focusing given by this alternating gradient system
  A fundamental point of optics, and of accelerator strong focusing
Thin quadrupole
matrices

## Slide 9: Strong Focusing: Another View
  For this to be focusing, x’ must have opposite sign of x where these are coordinates of transformation of incoming paraxial ray
  Equal strength doublet is net focusing under condition that each lens’ focal length is greater than distance between them

## Slide 10: 1D Periodic Transport Matrix
Periodic focusing systems are extremely useful
  (not just in accelerators: solid state, quantum, ...)
Examples:
  Rings (synchrotrons, betatrons): periodic once per “turn”
    Often “superperiodic”, more than once per turn
  Repeated lattices (FODO and other “cells”)
We need periodic focusing to keep beams stable
  Quadrupoles fortunately provide a linear restoring force
    Alternating focusing/defocusing provides net focusing
  Expect equations of motion to be like simple harmonic oscillators

## Slide 11: 1D Periodic Transport: Drifts and Quads (FODO)
Quadrupoles: phase space angle shear
Drifts: phase space position shear
  Dipoles: position shear with a little bit of rotation

## Slide 12: Warning: Professoral Egoistic Indulgence
Differential Equations Ahead
The following illuminates a connection between 2nd order linear differential equations and matrices that your lecturer finds beautiful so you will suffer through it

## Slide 13: Math: Hill’s Equation
Quadrupole equations of motion: linear restoring force
  What happens when we let the focusing K vary with s?
  Also assume K is periodic in s with some periodicity C
  This periodicity can be one revolution around the
  accelerator or as small as one repeated “cell”
  of the layout
  The simple harmonic oscillator equation with a
  periodically varying spring constant K(s) is
  known as Hill’s Equation

## Slide 14: Hill’s Equation Solution Ansatz
Solution is a quasi-periodic harmonic oscillator
  where w(s) is periodic in C but the phase Y(s) is not!!
  Substitute this educated guess (“ansatz”) to find
  For and to be independent of , coefficients of the sin and cos terms must vanish identically

## Slide 15: Courant-Snyder Parameters
Notice that in both equations so we can scale this out and define a new set of functions, Courant-Snyder Parameters or Twiss Parameters

## Slide 16: Towards The Matrix Solution
What is the matrix for this Hill’s Equation solution?
Take a derivative with respect to s to get
Now we can solve for A and B in terms of initial conditions
And take advantage of the periodicity of to find

## Slide 17: Hill’s Equation Matrix Solution
We can write this down in a matrix form where
is the betatron phase advance through one period C

## Slide 18: Parameterization of Periodic Transport
is independent of s
  the betatron phase advance of this periodic system
Determinant of matrix M is 1! (Liouville)
Equivalent to a rotation and some scaling
M can be written down in a beautiful and deep way
Twiss parameters
are periodic in C, but depend on s position within the periodic system
Describes 1D single particle and centroid linear motion over period C
(NB: Two transverse dimensions x,y are assumed decoupled here)
Matrix DeMoivre
Lie
algebras

## Slide 19: One Turn (or One Period) Map
http://www.toddsatogata.net/2019-USPAS/OneTurnMap.html

## Slide 20: Invariants and Ellipses
We assumed A was constant, an invariant of the motion
  A can be expressed in terms of initial coordinates to find
  This is known as the Courant-Snyder invariant: for all s,
  Similar to total energy of a simple harmonic oscillator
  looks like an elliptical area in phase space
  Our matrices look like scaled rotations (ellipses) in phase space
s=s0
s=s0+C
s=s0+2C
s=s0+3C

## Slide 21: Emittance
The area of the ellipse inscribed by any given particle in phase space as it travels through our accelerator is called the emittance : it is constant and given by
  Emittance is often quoted as the area of the ellipse that would contain a certain fraction of all (Gaussian) beam particles
  e.g. RMS emittance contains 39% of 2D beam particles
  Related to RMS beam size
  Yes, this RMS beam size depends on s!
  RMS emittance convention is fairly standard
  for electron rings, with units of mm-mrad

## Slide 22: Adiabatic Damping and Normalized Emittance
But constant-energy assumption is violated when we accelerate!
  When we accelerate, invariant emittance is not invariant!
  We are defining areas in phase space
  The definition of x doesn’t change as we accelerate
  But does since changes!
  scales with relativistic beta, gamma:
  This has the effect of compressing x’ phase space by
  Normalized emittance is the invariant in this case
    unnormalized emittance goes down as we accelerate
    This is called adiabatic damping, important in, e.g., linacs

## Slide 23: Floquet Transformation
All these one-turn (or one-period) maps are points around concentric ellipses
There must be a transformation that separates out the ellipse parameters and the circular rotation
This is called the Floquet Transformation

## Slide 24: Normalized Phase Space
If we define new coordinates then
and motion is just circles with the trivial solution

## Slide 25: Back to General Physical Solution
Particle position motion scales like
For ellipse aspect ratio

## Slide 27: General Linear Beam Transport
The normalized phase space transformation gives us a clever path to general linear beam transport
  From one location (s1) to another (s2)
  Rotation is just a portion of the phase advance, not the full tune
  Floquet transformations can use different Twiss Parameters (reminder: they depend on s coordinate!)

## Slide 28: General Linear Transport Matrix
We can parameterize a general non-periodic transport matrix from s1 to s2 using lattice parameters and
This does not have a pretty form like the periodic matrix
  However both can be expressed as
  where the C and S terms are cosine-like and sine-like; the second row is the s-derivative of the first row!
  A common use of this matrix is the m12 term:
Effect of angle kick
on downstream position

## Slide 29: General Linear Transport Matrix
So we have a very general form from all this math:
  with
  This is how one can parameterize uncoupled x or y transport from one location s1 to another location s2 where the Twiss parameters of those locations and their relative phase advance is known
    Such as from a table from a modeling code like madx
  Most modeling codes can also output matrix elements between specific locations at starts or ends of magnets

## Slide 30: Twiss Parameter Propagation
Labeling the transport matrix elements as m12 etc:
then we (okay, you) can show
and the phase advance between two locations is
also related to the transport matrix elements and
initial Twiss parameters by

## Slide 31: Review

## Slide 32: Lattice Optics: FODO Lives! (Be very careful in comparisons to other sources!)
Most accelerator lattices are designed in modular ways
  Design and operational clarity, separation of functions
One of the most common modules is a FODO module
  Alternating focusing and defocusing “strong” quadrupoles
  Spaces between are combinations of drifts and dipoles
  Strong quadrupoles dominate the focusing
  Periodicity is one FODO “cell” so we’ll investigate that motion
  Horizontal beam size largest at centers of focusing quads
  Vertical beam size largest at centers of defocusing quads
cell

## Slide 33: Periodic Example: FODO Cell Phase Advance
Select periodicity between centers of focusing quads
  A natural periodicity if we want to calculate maximum b(s)
  only has real solutions (stability) if
cell

## Slide 34: Periodic Example: FODO Cell Beta Max/Min
What is the maximum beta function, ?
  A natural periodicity if we want to calculate maximum b(s)
  Follow a similar strategy reversing F/D quadrupoles to find the minimum b(s) within a FODO cell (center of D quad)
cell

## Slide 35: FODO Betatron Functions vs Phase Advance
Generally want /L small
Strong focusing
Smaller magnets
Less expensive accelerator
[deg]
Here there be dragons

## Slide 36: FODO Beta Function, Betatron Motion
This is a picture of a FODO lattice, showing contours of since the particle motion goes like
  This also shows a particle oscillating through the lattice
  Note that provides an “envelope” for particle oscillations
    is sometimes called the envelope function for the lattice
  Min beta is at defocusing quads, max beta is at focusing quads
  6.5 periodic FODO cells per betatron oscillation
design trajectory
Betatron motion
trajectory

## Slide 37: Example: RHIC FODO Lattice
1/6 of one of two RHIC synchrotron rings, injection lattice
  FODO cell length is about L=30 m
  Phase advance per FODO cell is about
Horizontal
Vertical

low-beta insertion
FODO
low-beta insertion
matching
quadrupoles
dipoles

## Slide 38: Stability Diagrams
Designers often want or need to change the focusing of the two transverse planes in a FODO structure
  What happens if the focusing/defocusing strengths differ?
  Recalculate the M matrix and use dimensionless quantities
  then take the trace for stability conditions to find
cell

## Slide 39: Stability Diagrams II
  For stability, we must have
  Using , stability limits are where
  These translate to a FODO “necktie” stability diagram

## Slide 40: Triplet Optics: Extra Straight Space
cell
half quad!
half quad!
From R. Chehab et al., “The CLIC Positron Capture and Acceleration in the Injector Linac”, 2010.

## Slide 41: Triplet Optics: Extra Straight Space
cell
full double strength quad!
From R. Chehab et al., “The CLIC Positron Capture and Acceleration in the Injector Linac”, 2010.
symmetric beta
antisymmetric alpha
long drift
More this
afternoon

## Slide 42: Continuous Twiss Parameter Plot: RHIC IR